## Slide 1: Chapel 1.31/1.32 Release Notes: GPU Support
Chapel Team
June 22, 2023 / September 28, 2023

## Slide 2: GPU Support Outline
Background
Features
Portability
Performance
Next Steps
Notes: Use this for the deck’s top-level outline
Can also use it for a sub-outline within a topic with multiple parts, if/when we have any of those

## Slide 3: Background

## Slide 4: GPU Support
Background
We are adding native GPU support to Chapel
  A highly desired feature, given the potential to be a clean and portable way of programming GPUs
  GPUs are more and more common in supercomputers
    Over 95% of the compute capability on Frontier (currently #1 on the top-500) comes from its GPUs
In earlier releases, we’ve…
  …moved from an idea (1.23), to a demo (1.24), to a user-accessible feature on NVIDIA GPUs (1.25), …
  …to being able to drive multiple GPUs on one locale (1.26), and then multiple locales (1.27).
  We started to focus on performance and portability during 1.29 / 1.30
  1.31 / 1.32: continued push on performance and portability, responded to uptick in user requests
    Performance: optimizations impacting many benchmarks, ability to use Chapel tasks with GPUs
    Portability: AMD/NVIDIA parity, initial support for CUDA 12/ROCm 5, new cpu-as-device mode
    Community: new users trying out GPU support, significant increase in GitHub interactions
    Also new features for users and capabilities for developers

## Slide 5: GPU Support
GitHub Activity Summary
GPU support has started to receive attention
Before 1.30:
  2 user-reported issues were opened
Between 1.30 and 1.32:
  we had 21 user-reported issues
During 1.31/1.32, we prioritized resolving user issues
  we closed 27 total issues,
  14 of them were reported by users
We also started to report issues publicly ourselves
  ... while migrating internal discussions to the public repo

## Slide 6: Crash Course in GPU Programming Using Chapel

## Slide 7: GPU Support
Vector Increment Example: Basics
      on here.gpus[0] {
      var GpuVec: [1..n] int;
      GpuVec += 1;
      writeln(GpuVec);
      }
'on' statement targets a GPU
array data will be allocated on the targeted GPU
data-parallel operations will launch as a GPU kernel

## Slide 8: GPU Support
Vector Increment Example: Data Offload via Bulk Array Assignment
      var CpuVec: [1..n] int;
      on here.gpus[0] {
      var GpuVec = CpuVec;
      GpuVec += 1;
      CpuVec = GpuVec;
      }
      writeln(CpuVec);
host-to-device copy
device-to-host copy

## Slide 9: GPU Support
Vector Increment Example: Multiple GPUs via 'coforall'
      var CpuVec: [1..n] int;
      coforall gpu in here.gpus do on gpu {
      const myChunk = ...;
      var GpuVec = CpuVec[myChunk];
      GpuVec += 1;
      CpuVec[myChunk] = GpuVec;
      }
      writeln(CpuVec);
'coforall' creates a task per local GPU
a slice of the data is copied
between host and device

## Slide 10: GPU Support
Vector Increment Example: Multiple GPUs on Multiple Locales
      var CpuVec: [1..n] int;
      coforall loc in Locales do on loc {
      coforall gpu in here.gpus do on gpu {
      const myChunk = ...;
      var GpuVec = CpuVec[myChunk];
      GpuVec += 1;
      CpuVec[myChunk] = GpuVec;
      }
      }
      writeln(CpuVec);
'coforall' over all locales

## Slide 11: GPU Support
Vector Increment Example: Multiple GPUs using Multiple Tasks on Multiple Locales
      var CpuVec: [1..n] int;
      coforall loc in Locales do on loc {
      coforall gpu in here.gpus do on gpu {
      coforall workerId in 0..<numTasks {
      const myChunk = ...;
      var GpuVec = CpuVec[myChunk];
      GpuVec += 1;
      CpuVec[myChunk] = GpuVec;
      }
      }
      }
      writeln(CpuVec);
'coforall' to create multiple tasks per GPU
This pattern has significantly
improved performance in 1.32
See the "Performance" part of this deck.

## Slide 12: GPU Support
Overview of Changes in 1.31 and 1.32
Performance:
  Faster array access in kernels
  Faster Math library calls
  Faster multitasking on GPUs
  Turned the faster memory strategy on by default
  Peer-to-peer access features and exploration
Portability:
  CPU-as-Device mode
  AMD/NVIDIA feature and performance parity
  Initial Intel exploration
  CUDA 12/ROCm 5 support
New Features and Capabilities:
  Standalone atomic functions
  '--report-gpu' compiler flag
  Ability to compile for multiple NVIDIA architectures
  Improved debugging features:
    Ability to inspect assembly for AMD GPUs
    Improved auto-generated kernels' names
    New loop attribute '@assertOnGpu'

## Slide 13: Features
Atomic Operations
'--report-gpu' flag
Assembly Inspection
'@assertOnGpu' attribute
Multi-arch compilation
Improved Kernel Naming
Notes: Use this for the deck’s top-level outline
Can also use it for a sub-outline within a topic with multiple parts, if/when we have any of those

## Slide 14: Atomic operations on gpu
Background: GPUs have support for atomic operations (add, compare-and-swap, etc.)
This Effort: Added the following procedures for atomic operations to the GPU module:
      gpuAtomicAdd gpuAtomicMin gpuAtomicDec gpuAtomicXor
      gpuAtomicSub gpuAtomicMax gpuAtomicAnd gpuAtomicCAS
      gpuAtomicExch gpuAtomicInc gpuAtomicOr
Status: Almost all operations are supported on NVIDIA and AMD GPUs
  Caveat: 64-bit, signed, atomic 'min' and 'max' operations do not work when compiling for AMD
    These operations are not supported in HIP version < 5.7 (we currently support 4.0–5.4)
    We produce a compile-time error if these are used and 'CHPL_GPU=amd' is set
Next Steps:
  Allow using variables with Chapel's 'atomic' type and have them lower to these calls as appropriate (#23619)
  Enable atomic min and max on AMD GPUs once we support HIP versions >= 5.7
Notes: For the lack of signed hip operations compare https://sep5.readthedocs.io/en/latest/Programming_Guides/Kernel_language.html?highlight=atomicAdd#atomic-functions and https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html#atomicmax
https://github.com/ROCm-Developer-Tools/HIP/issues/3340

## Slide 15: --report-gpu flag
Background: Chapel generates kernels for all GPU-eligible loops
  Users may want to know what loops are and are not GPU-eligible
  'assertOnGpu' does a compile-time eligibility check, but needs to be applied manually to all loops
This Effort: Added '--report-gpu' to chpl to dump loop eligibility information
  We report on all loops that are order-independent and not already in a GPU kernel
Impact: The following code produces the following output when compiled with '--report-gpu':
foreach i in 0..10 do A[i] = callToExtern();
foreach i in 0..10 do A[i] *= 2;
foreach i in 0..10 do A[i] += 2;
      GPU INELIGIBLE LOOPS:
      ---------------------
      foo.chpl:1
      GPU ELIGIBLE LOOPS:
      -------------------
      foo.chpl:2
      foo.chpl:3
Next Steps: Consider increasing the verbosity for when we report GPU-ineligibility (#23620)

## Slide 16: Emitting gpu assembly with --savec flag
Background: --savec dumps code that can help users gain performance insights
  When using the C backend, it saves C files
  When using LLVM, it saves various llvm-related intermediate files
    (the name "savec" needs to change, at least for LLVM, see #18602)
  When compiling for NVIDIA GPUs, it also stores a PTX assembly file
    but previously we did not do this for AMD
This Effort: Ensured --savec outputs GPU-related assembly for NVIDIA and AMD
Impact:
  Regardless of GPU target, we output a 'chpl__gpu.s'
  In the generated assembly, kernels are named 'chpl_gpu_kernel_<fileName>_line_<num>'
  We now documented this in the technote and intend to support it going forward

## Slide 17: assert-On-Gpu Attribute
Background:
  Ensuring that loops were GPU-eligible was handled by a special 'assertOnGpu( )' function
  Calls to 'assertOnGpu( )' were either compile-time or run-time depending on its position, which was unusual
    If 'assertOnGpu( )' was a top-level statement in an ineligible loop, compiler reported an error immediately
This Effort:
  Use recently-added loop attributes to introduce '@assertOnGpu', which always performs a compile-time check
  Precludes the need for differentiating function behavior if it’s at the top level
      @assertOnGpu
      foreach a in A do a += 1;
Status:
  '@assertOnGpu' is the preferred way to check GPU eligibility
    the standalone 'assertOnGpu' function is deprecated
Next Steps:
  Investigate if a runtime-only assertion (like 'assertOnGpu()' not-at-top-level) is necessary

## Slide 18: Multi-Architecture GPU Executables
Background:
  It’s common for GPU-enabled programs to embed multiple GPU binaries for different architectures
    Enables a compiled program to run on devices with different GPU hardware
    e.g., a cluster with different GPU nodes, or a laptop with dedicated and integrated GPU
This Effort:
  Added prototypical support for multi-architecture executables to Chapel’s GPU functionality
Status:
  Initial support for multi-architecture executables for NVIDIA
    To access, pass comma-separated architectures to ‘--gpu-arch’
      > chpl --gpu-arch sm_70,sm_80
  Current approach relies on using the lowest-common version of PTX for named architectures
    with additional effort, could specialize PTX per architecture
Next Steps:
  Investigate additional specialization for architectures and multi-vendor support (#22783)

## Slide 19: GPU Kernel Naming
Background:
  Chapel generates GPU kernels by translating loops into procedures (named 'chpl_gpu_kernel')
  If multiple kernels are present, the built-in mangling appended '_1', '_2', and more
  However, 'chpl_gpu_kernel_1' isn’t very descriptive, and doesn’t make for easy debugging
This Effort:
  Change the GPU kernel naming policy to include the filename and line number. e.g.,
      chpl_gpu_kernel_fileName_line_13
      chpl_gpu_kernel_fileName_line_37
Status:
  Kernel naming changes are available in 1.32

## Slide 20: Portability
AMD/NVIDIA Parity
Intel Explorations
CPU-as-Device mode
CUDA 12/ROCm 5 support
Notes: Use this for the deck’s top-level outline
Can also use it for a sub-outline within a topic with multiple parts, if/when we have any of those

## Slide 21: GPU architecture Feature Parity
Background: In 1.30, some Chapel code was not portable across AMD and NVIDIA GPUs
  Specifically, using the 64-bit versions of these functions caused compile-time failures when building for AMD:
      acos acosh asin asinh atan atan2
      atanh cbrt cosh erf erfc ldexp
      lgamma log1p sinh tan tanh tgamma
This Effort: Fixed a bug causing us to erroneously link to the wrong version of these math functions
Status: We now support the same math functions for NVIDIA and AMD
Notes: PR: https://github.com/chapel-lang/chapel/pull/22791
For the lack of signed hip operations compare https://sep5.readthedocs.io/en/latest/Programming_Guides/Kernel_language.html?highlight=atomicAdd#atomic-functions and https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html#atomicmax
https://github.com/ROCm-Developer-Tools/HIP/issues/3340
It got added:
https://github.com/ROCm-Developer-Tools/clr/blob/5914ac3c6e9b3848023a7fa25e19e560b1c38541/hipamd/include/hip/amd_detail/amd_hip_atomic.h#L825

## Slide 22: Gpu architecture performance Parity
Background: In 1.30, HPCC-Stream was competitive with CUDA on NVIDIA but not with HIP on AMD
This Effort: Updated runtime to avoid calling a deprecated HIP API
Impact: Stream now performs competitively to C+HIP on AMD
Notes: This is the API in question: https://github.com/chapel-lang/chapel/pull/22375/files hipHostAlloc -> hipHostMalloc

## Slide 23: Targeting Intel GPUs
Background:
  Chapel supports targeting NVIDIA and AMD GPUs; but Intel GPUs are not supported, yet
    LLVM does not support targeting Intel GPUs
This Effort:
  We investigated Intel's LLVM-based 'dpc++' compiler
    Discovered that default builds may not be suitable for use as the system LLVM
    Headers and some tools are missing
Next Steps:
  Allow Chapel to be built with Intel's LLVM as the system LLVM
    Create documentation for it for advanced users
  Implement a runtime layer for Intel GPUs based on oneAPI Level Zero

## Slide 24: CPU-as-Device Mode
Background and This Effort
Background:
  Chapel's GPU support required the runtime to be built with CUDA or HIP as a dependency
    This meant that even simple development must be done on a system with actual GPUs
  Being able to start HPC-oriented development on a personal computer is an important part of productivity
    e.g., Chapel also allows multilocale development on a personal computer
This Effort: Chapel now has a cpu-as-device mode for GPU programming without GPUs
  No CUDA/HIP dependencies, no need for actual GPUs
  To enable this mode:
      > export CHPL_LOCALE_MODEL=gpu # required for GPU support in general
      > export CHPL_GPU=cpu # mandatory to enable cpu-as-device mode. i.e., will never be set automatically

## Slide 25: CPU-as-Device Mode
Status
Compiler works similarly, but the original loop will always execute
Runtime's calls bump up diagnostic counters as appropriate, redirect to other parts of the runtime
  i.e., GpuDiagnostics can be used normally in most cases
'@assertOnGpu' on a loop generates:
  Compiler error: if the loop is not GPU-eligible
  Runtime warning: if the loop is run on a non-GPU locale
    The warning can be disabled by setting the 'CHPL_GPU_NO_CPU_MODE_WARNING' environment variable
if (on_gpu()) {
launch_kernel(...);
}
foreach i in 1..n do
foo();
foreach i in 1..n do
foo()
Translates
into
Runtime code:
void launch_kernel(...) {
num_launches += 1;
return;
}

## Slide 26: CPU-as-Device Mode
Next Steps
We plan to address some behavior differences we observed
  Nested GPU-eligible loops cause GpuDiagnostics to register more kernel launches than expected
  Argument passing and outer variable usage details are not captured in this mode
    We were unable to reproduce some actual GPU bugs in this mode
  The generated kernel is discarded while generating the final code
    There's no generated kernel code that is very useful for advanced debugging during development
if (on_gpu()) {
launch_kernel(...);
}
else { // need 'else' now
foreach i in 1..n do
foo();
}
foreach i in 1..n do
foo()
Will translate
into
Runtime code:
void launch_kernel(...) {
num_launches += 1;
for (int threadIdx...
call_kernel(kernel,
threadIdx,
...);
return;
}

## Slide 27: CUDA 12.x Support
Background:
  Chapel supported CUDA 11.x and 10.x with some limitations
  CUDA 12.x was not supported before
    Main blocker: LLVM/Clang 15 (highest version Chapel supports) does not support CUDA 12.x
    Noted by multiple users
  LLVM/Clang 16 supports CUDA 12
This Effort:
  We patched our bundled LLVM (version 15) to support CUDA 12
  Unsupported versions generate an error while building Chapel
  Status:
  CUDA 12 is now supported only when using the bundled LLVM
Next Steps:
  Complete LLVM 16 upgrade to enable CUDA 12 support with system LLVM too
  Consider dropping CUDA 10.x support
    Should be a documentation change only: we do not maintain any code to support 10.x specifically

## Slide 28: ROCM 5.x Support
Background:
  Chapel supported ROCm 4.x
  ROCm 5.x was not tested before
  Status:
  Unsupported versions generate an error while building Chapel
  5.0, 5.1: Fully supported
  5.2-5.4: Supported, but deprecation warnings from clang are expected
    The way the compiler uses a clang tool to bundle device and host binaries is deprecated
    We plan to fix this soon
  5.5+: Not supported
    These versions require LLVM 16
    There may be a way to use LLVM 15, or patch it similarly to LLVM 16
    For now, we are waiting on the LLVM 16 upgrade
  5.7+: Not supported, but required for 64-bit, signed 'gpuAtomicMax' and 'gpuAtomicMin' support
  See #23480 for the most up-to-date status of ROCm 5.x support

## Slide 29: Performance
Faster Array Access
Peer-to-Peer Access
Array-On-Device
Task Parallelism with GPUs
Faster Math Library Calls
GPU Specialization
Notes: Use this for the deck’s top-level outline
Can also use it for a sub-outline within a topic with multiple parts, if/when we have any of those

## Slide 30: Faster Array Access in Kernels
Background and This Effort
Background:
  Arrays have two layers of indirection to get to underlying data
  Loop Invariant Code Motion (LICM) is an optimization that moves code from inside to outside a loop
    Helps avoid repetitive computations that always have the same value (e.g., 1+1).
    Can be used to move array metadata access, too
  Chapel’s LICM optimization is conservative; arrays passed by reference are not considered “constant”
      proc copyArray(ref A: [?D] int, ref B: [D] int) {
      foreach i in A.domain do B[i] = A[i];
      }
This Effort:
  Arrays passed by reference to GPU kernels won’t be changed from outside
    Relax LICM rules to match
Result:
4 metadata accesses per iteration!

## Slide 31: Faster Array Access in Kernels
Impact
Performance improvements across multiple benchmarks
4 metadata accesses total!
proc copyArray(ref A: [?D] int, ref B: [D] int) {
foreach i in A.domain do B[i] = A[i];
}
2.1x faster
SHOC Triad kernel
1.25x faster
SHOC Sort kernel

## Slide 32: Peer-to-peer access
Background and This Effort
Background:
  GPUs can communicate directly with one other
    Can be through PCIe or communication links such as NVLink or Infinity Fabric
  Previously, Chapel's GPU runtime would not enable peer-to-peer communication
This Effort: Create a way to enable peer-to-peer communication
  Added the 'enableGpuP2P' config constant to 'GPU' module
    To use, run your Chapel program with '--enableGpuP2P=true'

## Slide 33: Peer-to-peer access
Impact
 | 0 | 1 | 2 | 3
0 |  | 13.2 | 11.9 | 13.3
1 | 13.2 |  | 13.4 | 13.5
2 | 13.2 | 13.3 |  | 13.5
3 | 13.2 | 13.2 | 13.4 | 
Throughput (GiB/s)
enableGpuP2P=false
 | 0 | 1 | 2 | 3
0 |  | 86.2 | 86.3 | 86.3
1 | 86.1 |  | 86.4 | 86.3
2 | 86.6 | 86.5 |  | 86.1
3 | 86.6 | 86.5 | 86.5 | 
Impact: On NVIDIA, we see close to 6x throughput improvement in GPU-to-GPU transfers
  Tables measure 8 GiB transfers on a system with 4 NVIDIA A100-SXM4 GPUs
  Row and column correspond to source and destination GPU
  Each transfer was performed individually
Throughput (GiB/s)
enableGpuP2P=true

## Slide 34: Peer-to-peer access
Status and Next Steps
Status: While NVIDIA GPUs benefit from '--enableGpuP2P', AMD GPUs do not
  We have observed that AMD conducts peer-to-peer transfers by default
    On Frontier we see ~10–47 GiB/s transfers in our benchmark regardless of how '--enableGpuP2P' is set
  With AMD, setting 'HSA_ENABLE_SDMA=0' adjusts GPU-to-GPU transfers for higher throughput
    We observed up to 160 GiB/s transfer rates on Frontier with this setting
Next Steps:
  Find non-artificial benchmarks using peer-to-peer communication
  Further investigate peer-to-peer performance with AMD GPUs and Infinity Fabric
    Determine if we want Chapel to adjust 'HSA_ENABLE_SDMA'
  Determine if we should allow turning on/off peer-to-peer access on an individual GPU level (#23621)
    Or allow specifying peer-to-peer communication on an individual put/get basis
Notes: HAS_ENABLE_SDMA: when disabled communication occurs via kernel launch enabling faster transfers at the expense of being able to overlap communication and computation

## Slide 35: Array-On-Device
Unified Memory | Array on Device
0.12 | 0.18
0.038 | 0.018
18.16
Significantly improved
CPU array initialization
Unified Memory | Array on Device
0.25 | 0.033
0.14 | 0.034
var CpuArr: [1..n] int;
on here.gpus[0] {
var GpuArr: [1..n] int;
GpuArr = CpuArr;
CpuArr = GpuArr;
}
Time (s)
(RTX A2000)
Background:
  'array_on_device' is a memory strategy
    Faster data transfers and GPU array initialization
    However, CPU array initialization was sub-optimal
This Effort:
  Significantly improved performance
    Implemented GPU-aware GET/PUT calls
    This will also help GPU-driven communication
Status:
  'array_on_device' performs better
    1.2x – 14x improvements in nightly testing
  It is the default memory strategy as of 1.32
Performance in previous
release was lacking

## Slide 36: Avoiding Task Starvation
      on here.gpus[0] {
      begin {
      gpuData2 = cpuData2;
      data2Copied.writeEF(true); }
      foreach d in gpuData1 do foo(d);
      if data2Copied.readFE() then
      foreach d in gpuData2 do bar(d);
      }
Background
Communication and computation overlap is:
  An optimization to make use of different HW units
  An important technique in GPU programming
Chapel tasks are a natural way to achieve overlap
  However, before 1.32 task starvation prevented that
Core 0
pthread 0
task queue
<will sched. child tasks on core 0>
<will sched. child tasks on core 0>
<will sched. child tasks on core 1>
Task-private counter determines
the core on which child tasks will be scheduled
... which will happen only when it hits sync variable read
Result: No Overlap
This copy in 'begin' must wait b/c:
  it got scheduled behind the parent task
  current scheduler does not allow task stealing

## Slide 37: Avoiding Task Starvation
<will sched. child tasks on core 1>
      on here.gpus[0] {
      begin {
      gpuData2 = cpuData2;
      data2Copied.writeEF(true); }
      foreach d in gpuData1 do foo(d);
      if data2Copied.readFE() then
      foreach d in gpuData2 do bar(d);
      }
This Effort
With 1.32, a task yields right after launching a kernel
  In non-contentious cases, cost is not observable
  If tasks contend for a core, allows overlap
Core 0
pthread 0
task queue
<will sched. child tasks on core 0>
The parent task will yield after launching the kernel
Result: Overlap!
The copy in 'begin' can execute
The main task waits in the queue
while GPU kernel is executing

## Slide 38: Task-Parallel GPU Operations
      on here.gpus[0] {
      coforall worker in 0..#numWorkers {
      var DevIn, DevOut: [0..#tSize] real;
      while true {
      // dynamically pick the next chunk
      const myChunkId = curChunk.fetchAdd(1);
      if myChunkId >= numChunks then break;
      const myChunk = myChunkId*tSize..#tSize;
      DevIn = HostIn[myChunk]; // copy in
      kernel(DevIn, DevOut); // kernel
      HostOut[myChunk] = DevOut; // copy out
      }
      }
      }
To overlap communication/computation on a GPU:
  Data can be split into chunks
  Multiple CUDA/HIP streams do copy+kernel launch
  GPU driver can interleave copies with launches
    But they must come from different GPU streams
One way of doing that in Chapel is:
  Create multiple worker tasks per GPU
  Have each of them run a loop
  While picking the next chunk dynamically
  Until all the chunks are processed
Before 1.32, this would perform worse
  Non-overlapped version is faster
  Regardless of per-task size and/or number of tasks
Background

## Slide 39: Task-Parallel GPU Operations
Results in completely sequential order:
Previously, Chapel used the default GPU stream
  i.e., GPU operations from parallel tasks got serialized
Background
      on here.gpus[0] {
      coforall worker in 0..#numWorkers {
      var DevIn, DevOut: [0..#tSize] real;
      while true {
      // dynamically pick the next chunk
      const myChunkId = curChunk.fetchAdd(1);
      if myChunkId >= numChunks then break;
      const myChunk = myChunkId*tSize..#tSize;
      DevIn = HostIn[myChunk]; // copy in
      kernel(DevIn, DevOut); // kernel
      HostOut[myChunk] = DevOut; // copy out
      }
      }
      }
Core 0
worker=0
Core 1
worker=1
ops | t0 | t1 | t2 | t3 | t4 | t5
xfer | in |  | in |  | out | out
exec |  | kernel |  | kernel |  | 
time
Default GPU
Stream
copy in
copy in
copy out
kernel
kernel
GPU Driver

## Slide 40: Task-Parallel GPU Operations
This Effort: Per-task, per-device streams
  Each worker task will have its own GPU stream
This Effort and Impact
      on here.gpus[0] {
      coforall worker in 0..#numWorkers {
      var DevIn, DevOut: [0..#tSize] real;
      while true {
      // dynamically pick the next chunk
      const myChunkId = curChunk.fetchAdd(1);
      if myChunkId >= numChunks then break;
      const myChunk = myChunkId*tSize..#tSize;
      DevIn = HostIn[myChunk]; // copy in
      kernel(DevIn, DevOut); // kernel
      HostOut[myChunk] = DevOut; // copy out
      }
      }
      }
Per-task GPU
Streams
ops | t0 | t1 | t2 | t3 | t4 | t5
xfer | in | in | out | out |  | 
exec |  | kernel | kernel |  |  | 
Enables better overlap:
time
GPU Driver
copy in
copy in
kernel
kernel
copy out
Core 0
worker=0
Core 1
worker=1

## Slide 41: Faster Math Library Calls In Kernels
Background: Math library calls like 'sqrt' were unexpectedly slower compared to CUDA/HIP
  Reported by a user (#22112)
This Effort: The performance issue is fixed in 1.32
  The compiler was generating calls that were wrapped in some helper functions that should have been inlined
  The root issue was the ordering of device library linkage w.r.t. the LLVM optimization pipeline
Impact: Math library functions perform on-par with CUDA/HIP
  Two mini-applications benefitted from this optimization
 | Speedup | 
 | NVIDIA A100 | AMD MI250X
coral | 1.80x | 1.25x
miniBUDE* | 1.82x | 1.92x
* https://github.com/xianghao-wang/miniBUDE/tree/benchmark

## Slide 42: GPU Specialization
GPU-eligible loops exhibit different behavior depending on if you are on a GPU locale or not
  Namely, if we are on a GPU locale then we do a kernel launch
Checking to see if we are on a GPU adds overhead at every eligible loop
  Note the repeated execution of the 'if' statement in this example:
  on loc do
  for i in 0..<N do
  foreach k in 0..<P do ...
  on loc do onBody()
  proc onBody() do
  for i in 0..<N do
  if is_gpu_locale(here) then
  gpu_kernel_launch(extractedLoopFunc, ...)
  else
  foreach k in 0..<P do ...
The compiler "lowers" this to:
Original code:
Background
body of 'on' statement is outlined into a function
  since the 'foreach' loop is GPU-eligible, we insert a runtime check to see if we are on a GPU locale. If so, launch it as a kernel.

## Slide 43: GPU Specialization
This Effort
Clone functions reachable from 'on' statements into ”GPU-specialized" and "non-GPU-specialized" copies
  Rewrite calls in GPU-specialized functions to call other specialized functions
  Perform a runtime check to see if you are on a GPU in the 'on' statement; if so, call the cloned function
  on loc do
  for i in 0..<N do
  foreach k in 0..<P do ...
  if is_gpu_locale(loc) on loc do onGpuBody();
  else on loc do onBody();
  proc onGpuBody() do
  for i in 0..<N do
  gpu_kernel_launch(extractedLoopFunc, ...)
  proc onBody() do
  for i in 0..<N do
  if current_sub_locale >= 0 then
  gpu_kernel_launch(extractedLoopFunc, ...)
  else
  foreach k in 0..<P do ...
Lowers to
this specialization can avoid the runtime check
in theory this could too, but we don't currently
account for virtual function calls,
so we still do it here
Notes: We can safely assume gpuBody is executed on a GPU locale, so we no longer have the 'if' statement here
We should be able to accomplish the same here, but our analysis doesn't currently account for virtual function calls. As such, we can not guarantee this function is on a CPU locale and still need to perform the check.

## Slide 44: GPU Specialization
Impact and Status
Impact: Current limitations prevent us from improving performance
  In an unsafe version, we see a 3x performance improvement
    Unsafe because it does not rewrite virtual function calls in GPU-specialized functions to call GPU-specialized clones
  In our current safe version of the transform, we do not see a performance improvement
    Safe because we do not remove 'if' statements from non-GPU-specialized functions
  Adding extra functions also increases compile time (~30% longer in some cases)
Status: The transform is considered experimental and may be beneficial in the future
  It can optionally be turned on by passing '--gpu-specialization' to 'chpl'
  Aside from removing a per-eligible-loop runtime check, the transform may prove useful for other optimizations:
    specializing reductions on GPU locales
    less aggressive wide pointer usage

## Slide 45: GPU Specialization
Next Steps
Study more benchmarks, examining overhead from using the GPU locale model on non-GPU bound code
Make the transform cognizant of virtual function calls
Avoid overspecialization when unnecessary
Explore other kinds of specialization that may not add as much compile-time overhead

## Slide 46: Summary & Next Steps

## Slide 47: GPU Support
Summary: Highlights from 1.31 and 1.32
Performance:
  Faster default memory strategy: 1.2x – 14x improvement on several benchmarks
  Faster array access in kernels: 1.1x – 2x improvement on several benchmarks
  Faster Math library calls: 1.3x – 1.9x improvement on two applications
  Can reach peak peer-to-peer bandwidth on Frontier
Portability:
  Feature and performance parity between NVIDIA and AMD targets
  CPU-as-Device mode
Features:
  Atomic operations
  Ability to compile for multiple NVIDIA architectures
  Increased introspection through: '--report-gpu', '--savec' on AMD and improved kernel naming

## Slide 48: GPU Support
Proposed Next Steps for 1.33 and 1.34
Portability:
  Improve cpu-as-device behavior parity
  Improve CUDA 12/ROCm 5 support with LLVM 16
Explorations:
  Try using dpc++ as the system LLVM for Intel GPUs
  Start working on GPU-driven communication
  Investigate launching multidimensional grids
  Start improving CPU/GPU portability
Features:
  Foreach intents and better shadowing
  Warp-/wavefront-level functions
    warp-synchronization
    data shuffle
  Initial support for basic whole-array reductions
  Prototype syntax for advanced forall features
Performance:
  Continue investigating low-performance cases
  Investigate non-GPU execution performance
  Outer-loop vectorization for CPU

## Slide 49: Other GPU Improvements

## Slide 50: other GPU improvements
For a more complete list of GPU support changes and improvements in the 1.31 and 1.32 releases, refer to the following sections in the CHANGES.md file:
  ‘GPU Computing’
  ‘Bug Fixes for GPU Computing’

## Slide 51: Thank you
https://chapel-lang.org
@ChapelLanguage